## Slide 1: b10011 Numerically Awesome
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Acknowledgements
The Great Wikipedia, Finder of Figures
John Carmack, Quake III Arena Source Code
Ray Andraka: A survey of CORDIC algorithms for FPGA based computers
Lumilogic
Jack E. Volder, The CORDIC Trigonometric Computing Technique

## Slide 3: Today
Manipulating Formulae for Fun and Profit
Polynomial Fits
Newton Raphson
CORDIC

## Slide 4: Manipulating Formulae
Welcome to Algebra 404
  Where Math don’t think it be like it is, but it do.
Use algebra to reformat for “good” execution
  Execution Speed
  Code Size
  Accuracy

## Slide 5: Easy Speed Tweaking
Look for degenerate expensive cases
Look for duplicated effort and eliminate it
Plan your loads / stores carefully!

## Slide 6: Multiplication Tricks
Sometimes, shift-add is cheap
  9x = 8x + x = X<<3 + X
  In Arm and Thumb(2), this is one instruction
  add $r1, $r0, $r0 lsl 3
Two ops, One Instruction?
  Why?
Multiplicands with a small number of active bits

## Slide 7: Two Ops, One Instruction
This is a clue about:
  What types of programs this processor runs
  What instructions those programs have
DSPs often have Multiply Accumulate
  X += Y*Z
  X might be fixed: The Accumulator (register)
    This might even be a wide register!

## Slide 8: Booth Encoding
Represent the multiplicand as runs of ones
  X*60d = X * b00111100
Runs of Ones are the difference of powers of 2
  60 = 64 – 4 = 2^6 – 2^2
  X*60 = X<<6 – X<<2
There are many other fixed multiplicand tricks

## Slide 9: Polynomials
“Human” Form:
Ax^3+Bx^2+Cx^1+Dx^0
How many Multiplies does this use? Adds?
Notes: Multiply : 3+2+1 = 6
Add: 3

## Slide 10: Polynomials
“Human” Form:
Ax^3+Bx^2+Cx^1+Dx^0
How many Multiplies does this use? Adds?
  Ax^3 = 3 Multiplies
  Bx^2 = 2 Multiplies
  … 6 Mults, 3 Adds
Notes: Multiply : 3+2+1 = 6
Add: 3

## Slide 11: Polynomials
“Human” Form:
Ax^3+Bx^2+Cx^1+Dx^0
(Paraphrased) Horner’s Scheme
((((Ax)+B)x+C)x+D)
Now how many?
Notes: Multiply : 3+2+1 = 6
Add: 3
Multiply: 3
Add : 3

## Slide 12: Polynomial Approximations
Goal: Approximate a transcendental as a poly
Attempt 1: Taylor Series
Create a LUT for several values of a
  Store f^n(a)/n!
Notes: Powerpoint sucks for formulas

## Slide 13: Polynomial Approximation
How deep should the LUT be?
  Deeper means we are on average closer
  Better approximation for a given number of terms
  But Deeper also means more expensive
  No easy answer 
How do you pick a?
  Right in the middle of your range

## Slide 14: Implementation: Poly/LUT
Find the nearest a in our LUT
  Truncate x, use as index in to table
Load Coefficients
  Sine and Cosine are special: Why?
Calculate with Horner’s Scheme

## Slide 15: Picking Coefficients
Taylor Series optimizes accuracy for x ≈ a
  Largest errors right between LUT points
Statistics has nice ways to optimize RMS error
  Does a better job of spreading the error
  But still not perfect
We care about the worst case error
  I haven’t found a great way to do this yet
  So I just brute force it with an annealing algorithm

## Slide 16: My Method
Prototype with double precision floats
  MATLAB, Python or Wolfram Alpha
  Count adds, mults, loads, etc
Move to integer math
  Python (X,Y)
  Any catastrophic loss of precision? Rearrange
  Anneal coefficients over a weekend
Automagically try several Depth/Power combos

## Slide 17: Approximation “Folding”
Make use of symmetry in your functions
  “Fold” the function in half cuts LUT depth in half!
One of my favorite assembly language games
  Great practice in number systems and asm tricks
How do you fold cos(x)?

## Slide 18: Fold cos(x)=cos(|x|)
x=abs(x) on MIPS
    slt $t1, $t0, $zero // $t0<0?
    beq $t1, $zero, negative // branch
    sub $t0, $zero, $t0 // negate
    negative:
x=abs(x) on MIPS
    sra $t1, $t0, 31 // -1 or 0
    xor $t0, $t0, $t1 // |x|-1 or x
    sub $t0, $t0, $t1 // |x|-1-(-1) or x-0
x=abs(x) on ARM
    cmp r0, #0 // Compare r0 to zero
    rsblt r0, r0, #0 // If <0, r0 = 0 – r0

## Slide 19: Further Trig Folding
Trig functions are periodic
  sin(x) = sin(x%2pi)
  In radians
modulo power of 2 is super easy
  Linearly scale so that 1 cycle is a power of 2
  Get rid of extra high bits

## Slide 20: Approximation Folding
How do you fold 1/x?
  1/x^2? e^x?
These have symmetry…
  But not in the linear way trig does
  Higher order symmetry
1/(x) = 2^-n/(x*2^n)

## Slide 21: Approximation Folding
These symmetries are harder to exploit
Count Leading Zeros
  Quick stand-in for log(2)
  Break spaces into powers of 2
  Shift by the number of leading zeros
  Compensate Later
This helps with limiting calculation Range!
  Optimize for accuracy instead of range

## Slide 22: Calculating Interesting Functions
GIANT LUTs
  Because we have silicon area to burn
  Area doubles per bit of accuracy
Power Series and LUTs:
  Approximation by polynomial
  More efficient in space, but still improves slowly
Lets find better ways
  That gain accuracy faster

## Slide 23: Newton Raphson
Successive approximation to find root of a well behaved function

## Slide 24: Newton Raphson Division
Want to find
  Create a function that crosses zero at that point
D=3

## Slide 25: Newton Raphson Division

## Slide 26: Newton Raphson Division
Quadratic Convergence
  Each step is twice as accurate as previous!
Hot Diggity!... but
  LUT, with symmetry
Must be within a Basin of Attraction
  Bad initial conditions will never converge

## Slide 27: Basin of Attraction
What does the black line represent?

## Slide 28: Basin of Attraction
Now it will never converge 

## Slide 29: Newton Raphson 1/sqrt
float Q_rsqrt( float number ) {
long i;
float x2, y;
const float threehalfs = 1.5F;
x2 = number * 0.5F;
y = number;
i = * ( long * ) &y; // evil floating point bit level hacking
i = 0x5f3759df - ( i >> 1 ); // what the fuck?
y = * ( float * ) &i;
y = y * ( threehalfs - ( x2 * y * y ) ); // 1st iteration
// y = y * ( threehalfs - ( x2 * y * y ) ); // 2nd iteration, this can be removed
return y;
}
Quake III Arena Source Code

## Slide 30: Initial Approximation
float Q_rsqrt( float number ) {
long i;
float x2, y;
const float threehalfs = 1.5F;
x2 = number * 0.5F;
y = number;
i = * ( long * ) &y; // evil floating point bit level hacking
i = 0x5f3759df - ( i >> 1 ); // what the fuck?
y = * ( float * ) &i;
y = y * ( threehalfs - ( x2 * y * y ) ); // 1st iteration
// y = y * ( threehalfs - ( x2 * y * y ) ); // 2nd iteration, this can be removed
return y;
}
Quake III Arena Source Code

## Slide 31: Newton Raphson Iteration
float Q_rsqrt( float number ) {
long i;
float x2, y;
const float threehalfs = 1.5F;
x2 = number * 0.5F;
y = number;
i = * ( long * ) &y; // evil floating point bit level hacking
i = 0x5f3759df - ( i >> 1 ); // what the fuck?
y = * ( float * ) &i;
y = y * ( threehalfs - ( x2 * y * y ) ); // 1st iteration
// y = y * ( threehalfs - ( x2 * y * y ) ); // 2nd iteration, this can be removed
return y;
}
Quake III Arena Source Code

## Slide 32: Translating to Fixed Point
Floating Point Newton Raphson is easy
  It handles range changes for you
Fixed Point is degenerately bad
  Intermediate steps are all over the place
Use symmetry to tighten up ranges
Be Careful!

## Slide 33: CORDIC
Multiplies are expensive in hardware
  So many adders!
Jack Volder invented CORDIC in 1959
  Trig functions using only shifts, adds, LUTs
  We’ll be looking at this half
John Stephen Welther generalized it at HP
  Hyperbolics, exponentials, logs, etc
  This half is awesome too

## Slide 34: CORDIC?
COordinate Rotation DIgital Computer
  A simple way to rotate a vector quickly
Creates rotation matrices based on 2^i
  Makes the math redonkulously quick

## Slide 35: Super Glossy Transformation Step
Start with the basic rotation matrix:
Use trig identities to transform to
Trust Me (or derive on your own)

## Slide 36: The Clever Bit
Pick values of to make the math easy
Now the rotation simplifies to
Store two separate look up tables
  … maybe

## Slide 37: CORDIC LUT
Calculated in advance
Stored in I?Q?
Look at
  Drop the table
  Just store 0.607253
0 | 45 | 0.707107 | 0.707107
1 | 26.56505 | 0.894427 | 0.632456
2 | 14.03624 | 0.970143 | 0.613572
3 | 7.125016 | 0.992278 | 0.608834
4 | 3.576334 | 0.998053 | 0.607648
5 | 1.789911 | 0.999512 | 0.607352
6 | 0.895174 | 0.999878 | 0.607278
7 | 0.447614 | 0.999969 | 0.607259
8 | 0.223811 | 0.999992 | 0.607254
9 | 0.111906 | 0.999998 | 0.607253
10 | 0.055953 | 1 | 0.607253
11 | 0.027976 | 1 | 0.607253
12 | 0.013988 | 1 | 0.607253
13 | 0.006994 | 1 | 0.607253
14 | 0.003497 | 1 | 0.607253
15 | 0.001749 | 1 | 0.607253
16 | 0.000874 | 1 | 0.607253
0 | 45 | 0.707107 | 0.707107
1 | 26.56505 | 0.894427 | 0.632456
2 | 14.03624 | 0.970143 | 0.613572
3 | 7.125016 | 0.992278 | 0.608834
4 | 3.576334 | 0.998053 | 0.607648
5 | 1.789911 | 0.999512 | 0.607352
6 | 0.895174 | 0.999878 | 0.607278
7 | 0.447614 | 0.999969 | 0.607259
8 | 0.223811 | 0.999992 | 0.607254
9 | 0.111906 | 0.999998 | 0.607253
10 | 0.055953 | 1 | 0.607253
11 | 0.027976 | 1 | 0.607253
12 | 0.013988 | 1 | 0.607253
13 | 0.006994 | 1 | 0.607253
14 | 0.003497 | 1 | 0.607253
15 | 0.001749 | 1 | 0.607253
16 | 0.000874 | 1 | 0.607253

## Slide 38: The Result
Rotating a vector is now:
  1 look up, 2 shifts, 3 adds
Optionally Compensate for magnitude at end
  1 lookup, 1 (difficult?) multiply

## Slide 39: Example: Finding the Phase
Given a vector, find
Plan:
Start with
Rotate vector into Quadrant I or IV
Rotate vector until it is flat (zero angle)
  At each iteration, choose direction by sign of Y

## Slide 40: Example: Finding the Phase
Find Phase of -1+3j
Rotate into a start Quadrant
  This is not yet CORDIC

## Slide 41: Example: Finding the Phase I=0
Iteration 0
Y is positive
  Rotate “Down”
)

## Slide 42: Example: Finding the Phase I=0
Iteration 0
Y is positive
  Rotate “Down”
-atan2^-0 from LUT
  =45 degrees
NOTE: Magnitude changed
  |-1+3j| != |4+2j|
)

## Slide 43: Example: Finding the Phase I=1
Iteration 1
Y is negative
  Rotate “Up”

## Slide 44: Example: Finding the Phase I=2
Iteration 2
Y is zero
  We are done!
.4
Actual answer?

## Slide 45: Example: Finding the Magnitude
Apply the compensations now
5

## Slide 46: Am I lucky or what?!
The example terminated nicely
  Do all start vectors terminate?
  Do all start vectors converge?
Explore the sequence
  How is it shaped?
Notes: Since it reduces slower than 2^-i, we will always converge!

## Slide 47: The Point?
Area increases linearly per bit of accuracy
Cheap Hardware
Very reusable

## Slide 48: With Remaining Time
Relax
  OR
Do any of these in Python / MATLAB / MIPS:
  CORDIC – Sine? Arcsine?
  Newton Raphson – invsqrt?
  Better than Taylor Approximation – annealing!

## Slide 50: With Remaining Time
Play with CORDIC
  What other functions can it calculate?
Continue with practice from before
Start HW3

## Slide 51: Group Work
Poly/LUT fit a transcendental function
  (Co)sine, e^x, or something else
  Pick a range
  Pick an accuracy – 24 bits?
Start with a Taylor approximation
  LUT Depth? Number of terms?
  What is your worst case error?
Try annealing a bit
  How much did it improve?
Create and Save Figures!
  We will discuss as a class

## Slide 52: With Remaining Time
Estimate how fast NR division runs in MIPS
  Each iteration cost: ?
Implement for x
  In floating point
Find appropriate IQ for intermediate calculations