## Slide 1: b1000 Single Cycle CPU
ENGR xD52
Eric VanWyk
Fall 2013

## Slide 2: Today
Intro to Memory
The Execution of an Instruction
Intro to Simple CPU Design
Assign Homework & Lab

## Slide 3: Memory
Look Up Table is a very simple memory
  Read One thing at a time
  Write nothing ever
Generically, a memory is defined by:
  Width & Depth
  Number and Type of Ports
    How many simultaneous read / write operations
  Speed (access time)

## Slide 4: Memory Attributes
Mutability:
  Read/Write
  Read Only
  Write Once
  Reprogrammable
Access Type
  Random
  Sequential
Volatility:
  Non-Volatile
  Volatile
  Refreshed

## Slide 5: Historical Side Note
History of Computer Memory is Amazing
  Consider it for your final project
Crazy Memory Types:
  Delay Line
    Sound waves through quartz/mercury
    Lasers reflected off the moom
  Williams Tube
    Cathode Ray Tube + Static Electricity

## Slide 6: Historical Memory: Core
http://en.wikipedia.org/wiki/Magnetic-core_memory

## Slide 7: Memories
We will devote several lectures entirely to memory
I will treat it as an opaque black box for this lecture, and open it in much more detail later
Your next lab is about memory interfaces

## Slide 8: Context
We now have almost all of the building blocks of a computer!
  Nearing completion of our first “spiral”
Today we will glance at the important ones
Moving forward we will dive deeper into each of these building blocks to expand capabilities

## Slide 9: Context
You will learn the dark arts of box opacity
Practice thinking hierarchically
So… what does a CPU do?

## Slide 10: CPU Execution Overview
Fetch instruction from memory
Decode instruction into actions/controls
Fetch/Decode operands
Compute result value or status
Push result(s) to storage
Determine next instruction
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 11: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 12: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 13: Processor Overview
Overall Dataflow
PC fetches instructions
Instructions select operand registers, ALU immediate values
ALU computes values
Load/Store addresses computed in ALU
Result goes to register file or Data memory

## Slide 14: Program/Instruction Memory
Large, single ported read-only memory
  For today
Stores the program the processor executes
Instructions are 4 bytes wide
  For today

## Slide 15: Register File
Very small, very fast multi-ported memory
  Small depth, large silicon area
Each cycle reads 2 words, optionally writes 1
This is the “scratch space” for the processor
This is homework soon
Aw Aa Ab Da
Dw Db
Register
WrEn File

## Slide 16: Assembly
The human readable version of the instructions the machine executes
Closely related to “Op Codes” and Instructions
We will go over this in detail soon.

## Slide 17: Instruction Decode
Today we are “black boxing” instructions
Blue Wires come from the Instruction Decoder
  Control signals that tell the CPU what to do
  E.g. ALU Control Lines
  Addresses

## Slide 18: Instruction RTL
RTL is Register Transfer Level
Short Hand for what the instruction should do
Reg[Rd] = Reg[Rs] & Reg[Rt]
Set the memory at location Rd equal to the data at location Rs boolean anded with the data at location Rt.

## Slide 19: Fetch Operands
Aw Aa Ab Da
Dw Db
Register
WrEn File
Rd Rs Rt
Get Operand Addresses
Pull from Register File
Reg[Rd] = Reg[Rs] & Reg[Rt]
Reg[Rs]
Reg[Rt]

## Slide 20: Execute
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
Rd Rs Rt
ALU controls from Instruction Fetch/Decode
Perform actual computation in ALU
Reg[Rd] = Reg[Rs] & Reg[Rt]
Reg[Rs] & Reg[Rt]

## Slide 21: Store Results
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Rd Rs Rt
Store the result back to the register file
Others Instructions have other effects
Reg[Rd] = Reg[Rs] & Reg[Rt]

## Slide 22: Using Constants
Sometimes we want to use a constant as an operand instead of a Register.
How do you encode a 32 bit constant AND control signals into a 32 bit instruction?
Side Note: The Cortex has interesting options
  any constant produced by shifting an 8-bit value
  any constant of the form 0x00XY00XY
  any constant of the form 0xXY00XY00
  any constant of the form 0xXYXYXYXY
Side Note: MIPS only has boring 16 bit constants

## Slide 23: Using Constants (Immediates)
Reg[rt]= Reg[rs]+SignExtend(imm);
How do we choose ALU Source?
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
SignExtnd
Imm16
Rs
Rt
Notes: Note that Aw is now connected to Rt instead of Rd. This is not an error – Rd occupies the same space as part of the immediate in the instruction, and is therefore not available for this instruction. This is resolved soon!

## Slide 24: Data Memory
Big Giant Slow Memory
  Gigabytes!
Read and Write, but only single port
  Write Enable (WrEn) switches between the two modes
Pulling from Data Memory to Register
  Load
Push from Register to Data Memory
  Store
WrEn Addr
Din Dout
Data
Memory

## Slide 25: Hook Up On The Boards
Create simple CPU with 4 types of instructions
  Listed on next Slide
Use the following Components
  ALU, Register File, Data Memory, Sign Extender
Use another marker color for control signals
To make a decision, use a MUX

## Slide 26: Quick Note on rd, rs, rt
Aw is inconsistent in the MIPS standard
  Sometimes rt
  Sometimes rd
This is ok!
  Makes other things clearer later
I don’t always have to choose between two signals, but when I do, I choose Multiplexor

## Slide 27: Hook Up On The Boards
Math with 2 Variables
Reg[rd] = Reg[rs] op Reg[rt];
Math with 1 variable and 1 constant
Reg[rt] = Reg[rs] op SignExtend(imm);
Load from data memory
Addr = Reg[rs] + SignExtend(imm);
Reg[rt] = Mem[Addr];
Store to data memory
Addr = Reg[rs] + SignExtend(imm);
Mem[Addr] = Reg[rt];

## Slide 28: One Possible Complete Datapath
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 29: With the remaining time
Work on Lab

## Slide 30: Using Constants (Immediates)
SignExtnd
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16
WrEn Addr
Din Dout
Data
Memory

## Slide 31: Datapath + Load
Addr = Reg[rs] + SignExtend(imm);
Reg[rt] = Mem[Addr];
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
RegDst
Rd
Rt
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16

## Slide 32: Datapath + Store
Addr = Reg[rs] + SignExtend(imm);
Mem[Addr] = Reg[rt];
Note: State of RegWr, MemToReg?
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Instruction
Fetch
Unit
Rs
Rt
Rd
Imm16