## Slide 1: b1001 Single Cycle CPU Continued
ENGR xD52
Eric VanWyk
Fall 2014

## Slide 2: Today
Instruction Decoding
Instruction Encoding
Continue Single Cycle CPU
Jumps and Branches

## Slide 3: Single Cycle Design Process
Instructions
RTL – Register Transfer Level
  Describes how the instruction is executed
  How information flows between registers
Schematic
  Arranges building blocks to implement RTL

## Slide 4: One Possible Complete Datapath
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 5: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 6: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 7: MIPS Code Encoding Formats
All instructions encoded in 32 bits
Register (R-type) instructions
Immediate (I-type) instructions
Jump (J-type) instructions
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
RD
SHAMT
FUNCT
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address
(OP = 0,16-20)
(OP = any but 0,2,3,16-20)
(OP = 2,3)

## Slide 8: I-Type
Used for ops with an immediate operand
One Op Field (Enumeration)
Two register address fields
One Signed/Unsigned field
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 9: I-Type Example
Register 7 = Register 2 + 15;
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 10: I-Type Example
Register 7 = Register 2 + 15;
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
addi = 8
2
7
15

## Slide 11: I-Type Example
Register 7 = Register 2 + 15;
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
addi = 8
2
7
15
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
001000
00010
00111
0000 0000 0000 1111

## Slide 12: Instruction -> CPU Controls
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
Rs
Rt
16 bit Address/Immediate
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 13: Instruction -> CPU Controls
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
Rs
Rt
16 bit Address/Immediate
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 14: Instruction -> CPU Controls
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
Rs
Rt
16 bit Address/Immediate
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg

## Slide 15: OP Decoding: LUT
Rs, Rt, Immediate, etc are directly passed
  Immediate gets sign extended
Op gets decoded to create other controls
  Record all signals in a table in human
  Translate to machine
  Implement as LUT

## Slide 16: Example Table
 | RegDst | RegWr | ALUcntrl | MemWr | MemToReg | ALUsrc
Math w/2 |  |  |  |  |  | 
Math w/ Imm |  |  |  |  |  | 
Load |  |  |  |  |  | 
Store |  |  |  |  |  | 

## Slide 17: Reg[rt] = Reg[rs] op SignExtend(imm);
 | RegDst | RegWr | ALUcntrl | MemWr | MemToReg | ALUsrc
Math w/2 |  |  |  |  |  | 
Math w/ Imm |  |  |  |  |  | 
Load |  |  |  |  |  | 
Store |  |  |  |  |  | 

## Slide 18: Reg[rt] = Reg[rs] op SignExtend(imm);
 | RegDst | RegWr | ALUcntrl | MemWr | MemToReg | ALUsrc
Math w/2 |  |  |  |  |  | 
Math w/ Imm | rt | TRUE | (op) | FALSE | ALU | IMM
Load |  |  |  |  |  | 
Store |  |  |  |  |  | 

## Slide 19: (op)?
Many ops will be extremely similar:
  Add immediate
  Add registers
  Subtract immediate
  Subtract registers
Synthesizer will optimize for size
  Repetition is something it is good at

## Slide 20: Behavioral Instruction Decoder LUT
“always @(…)” begins a behavioral block of code with a “sensitivity list”
Triggers on sensitivities
When OP changes, run this block of code
always @(OP)begin
case(OP)
opADDI: begin
RegDst =
RegWr =
ALUcntrl =
MemWr =
MemToReg =
ALUsrc =
end
endcase
end

## Slide 21: Behavioral Instruction Decoder LUT
Just like any other case statement you know and love
Equivalent to
  If(OP==opADDI) {…}
  Elseif(OP==???) {…}
always @(OP) begin
case(OP)
opADDI: begin
RegDst =
RegWr =
ALUcntrl =
MemWr =
MemToReg =
ALUsrc =
end
endcase
end

## Slide 22: Behavioral Instruction Decoder LUT
Assigns each of these control signals the appropriate value for the operation.
Copy this from your table
always @(OP) begin
case(OP)
opADDI: begin
RegDst =
RegWr =
ALUcntrl =
MemWr =
MemToReg =
ALUsrc =
end
endcase
end

## Slide 23: Behavioral LUT
“reg” for each output
  These will actually optimize away
  Only if written correctly!!!
Registers will stay (this is bad) if:
  One of your cases is incomplete
  You do not cover all cases
    default: helps with this.

## Slide 24: Our CPU So Far:
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Instruction
Decoder
Control
Signals
Instruction
Rd
Rt

## Slide 25: What boxes do we need?
Memory for Instructions
Something to “unpack” instructions
Memory for data
Something to compute stuff
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 26: Program Counter
Where are we in our program?
  Points to an instruction in program memory
Instructions are 4 bytes long in MIPS
Increment by 4 to get the next instruction

## Slide 27: Fetch Instruction
Instruction = Mem[PC]; // Fetch Instruction
PC = PC + 4; // Increment Program Counter
Adder
PC
Address
Instruction
Memory
Instr[31:0]
“4”
Notes: PC is a Register composed of edge triggered D Flip Flops.
Clock is missing from the diagram.

## Slide 28: Flow Control
for(int i = 0; i<N; i++) {
a = b + c;
b *= 3;
}
Jump – Unconditionally change PC
Branch – Conditionally change PC

## Slide 29: Flow Control
for(int i = 0; i<N; i++) {
a = b + c;
b *= 3;
}
Jump – Unconditionally change PC
  Jump back to the beginning of the loop
Branch – Conditionally change the PC
  Escape loop if i<N fails

## Slide 30: Add Flow Control
Modify the Instruction Fetch Unit to Branch:
  if ((Reg[rs] – Reg[rt]) == 0)
  PC = PC +4+ SignExtend(imm)*4;
  else
  PC = PC + 4;
Write RTL for your version of Jump
  What does Jump mean to you?
Implement your RTL
  What new control lines do you need?
  Any cool money saving tricks?
Create an instruction encoding for this

## Slide 31: Difficulties In Jumping
How did you define your Jump?
  Absolute: PC = New Value
  Relative: PC += Offset
Did you have enough bits?

## Slide 32: J-Type
Used for Unconditional Jumps
Simplest MIPS encoding
How do we encode “j 100”?
2: j (jump)
3: jal (jump and link)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address

## Slide 33: Jump RTL
Jump Instruction: j target
PC = { PC[31:28], target[25:0], “00” };
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address
Weirdness in the Address Field
Bottom 2 bits are always ‘00’, so drop them
  Shift everything over by 2
That’s only 28 effective bits…
  Where are the other 4?
  How does this limit us?
  How do we compensate?

## Slide 34: Jump RTL
Jump Instruction: j 100
PC = { PC[31:28], target[25:0], “00” };
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
2
25
Weirdness in the Address Field
Bottom 2 bits are always ‘00’, so drop them
  Shift everything over by 2
That’s only 28 effective bits…
  Where are the other 4?
  How does this limit us?
  How do we compensate?

## Slide 35: Complete Fetch Unit
SignExtnd
PC
Addr[31:2]
Addr[1:0]
Instruction
Memory
Concatenate
Adder
Instr[31:0]
Jump
“00”
PC[31:28]
Target Instr[25:0]
imm16
“1”
Zero
Branch
Cin
“0”

## Slide 36: Encoding Limitations
Designing an Encoding Scheme is a Game
  Best use of limited space?
  Favor some options over others
Take Available Space and divide into “Fields”
  Encoding within an Encoding (MOAR BOXES)
  Fixed width per field
  How many fields does IEEE-754 use?
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent

## Slide 37: Types of Fields
Enumerations
  No mathematical meaning, just enumerate options
Signed / Unsigned
  We know these well
Biased
  Mathematically offset by a constant

## Slide 38: I-Type
Used for ops with an immediate operand
One Op Field (Enumeration)
Two register address fields
One Signed/Unsigned field
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 39: J-Type
Used for Unconditional Jumps
Simplest MIPS encoding
How do we encode “j 100”?
2: j (jump)
3: jal (jump and link)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
26 bit Address

## Slide 40: R-Type
Used for 3 register ALU operations
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
RD
SHAMT
FUNCT
00: sll
02: srl
03: sra
04: sllv
06: srlv
07: srav
08: jr
24: mult
26: div
32: add
33: addu
34: sub
35: subu
36: and
37: or
38: xor
39: nor
42: slt
00
(10-13 for FP)
Shift amount
(0 for non-shift)
add $8, $9, $10 # $8 = $9+$10
sll $8, $9, 6 # $8 = $9<<6
sllv $8, $9, $10 # $8 = $9<<$10
Op2
Op1
Dest
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
9
10
8
0
32
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
X
9
8
6
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
00
10
9
8
0
04

## Slide 41: RS RT RD
RD – Bits 11-15 RegFile Aw
  shares space with IMM, only used in R-type
  If used, always the destination of the result
RT – Bits 16-20 RegFile Aw or Ab
  Operand address in R-type and rarely in I-type (e.g. beq)
  Result destination address in most I-type
RS – Bits 21-25 RegFile Aa
  Operand address in R-type and I-type
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
RD
SHAMT
FUNCT
OP
RS
RT
16 bit Address/Immediate
OP
26 bit Address

## Slide 42: With Remaining Time
Create a 16 bit instruction encoding
  What will you change to fit?
    Number of Registers?
    Types of Operations allowed?
    Limited Operand s?
Questions:
  What did you trim to fit?
  How do you load a 32 bit immediate value?
Email to Comparch14@gmail.com
  Not graded
Needs to address these ops:
  Math
  Branch if zero
  Jump
  Load
  Store
  Load Immediate
    Composite Instruction?

## Slide 43: Revisiting ARM’s Immediates
In Thumb state in ARMv6T2 and later the 32-bit MOV instruction can load:
  any 8-bit immediate value, giving a range of 0x0-0xFF (0-255)
  any 8-bit immediate value, shifted left by any number
  any 8-bit pattern duplicated in all four bytes of a register
  any 8-bit pattern duplicated in bytes 0 and 2, with bytes 1 and 3 set to 0
  any 8-bit pattern duplicated in bytes 1 and 3, with bytes 0 and 2 set to 0.
These values are also available as immediate operands in many data processing operations, without being loaded in a separate instruction.
Create an Encoding Scheme to generate these Immediates
Copyright © 2010-2011 ARM. http://infocenter.arm.com/help/topic/com.arm.doc.dui0473c/DUI0473C_using_the_arm_assembler.pdf
Notes: 8 bits for the pattern
5 bits for rotate
Top few values are open!

## Slide 44: Create Your Own Instruction Encodings
Create an Encoding Spec that covers:
  ALU Operations with 2 register operands
  ALU Operations with immediate for one operand
  Load from Data Memory, Store to Data Memory
  Jump (What type?)
  Branch
Consider splitting your definition in to ‘types’
Design an Instruction Decoder for it
  Probably a LUT (plus other stuff?)

## Slide 45: Our Single Cycle CPU
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Instruction
Fetch
Unit
Rs
Rt
imm16
Branch
Jump
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Zero
Instruction
Decoder

## Slide 46: Complete Fetch Unit
SignExtnd
PC
Addr[31:2]
Addr[1:0]
Instruction
Memory
Concatenate
Adder
Instr[31:0]
Jump
“00”
PC[31:28]
Target Instr[25:0]
imm16
“1”
Zero
Branch
Cin
“0”

## Slide 47: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 48: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 49: J-Type
Weirdness in the Address Field
Bottom 2 bits are always ‘00’, so drop’em
  Shift everything over by 2
That’s only 28 effective bits…
  Where are the other 4?
  How does this limit us?
  How do we compensate?

## Slide 50: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
addi
$t1
$t0
100
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
beq
$a1
$a0
-11
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
lw
$t0
$t3
12
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 51: I-Type Examples
04: beq
05: bne
06: blez
07: bgtz
08: addi
09: addiu
10: slti
11: sltiu
12: andi
13: ori
14: xori
32: lb
35: lw
40: sb
43: sw
addi $t0, $t1, 100 # $t0 = $t1+100
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
8
9
8
100
beq $a0, $a1, -44 # if $a0 == $a1 GOTO (PC+4+FOO*4)
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
4
5
4
-11
lw $t3, 12($t0) # $t3 = Memory[$t0+12]
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0x23
8
11
12
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
OP
RS
RT
16 bit Address/Immediate

## Slide 52: Control Signals
Func | 100000 | 100010 | N/A | N/A | N/A | N/A
Op | 000000 | 000000 | 100011 | 101011 | 000100 | 000010
 | add | sub | lw | sw | beq | j
RegDst |  |  |  |  |  | 
ALUSrc |  |  |  |  |  | 
MemToReg |  |  |  |  |  | 
RegWr |  |  |  |  |  | 
MemWr |  |  |  |  |  | 
Branch |  |  |  |  |  | 
Jump |  |  |  |  |  | 
ALUCntrl | Add | Sub | Add | Add | Sub | X

## Slide 53: Processor Overview
Overall Dataflow
PC fetches instructions
Instructions select operand registers, ALU immediate values
ALU computes values
Load/Store addresses computed in ALU
Result goes to register file or Data memory